## Slide 1: Open vSwitch
2016.05.12
남 성 식(soninlight@gmail.com)

## Slide 2: OVS(Open vSwitch)
리눅스 기반의 가상 소프트웨어 스위치
Open source Apache 2 License
네트워크를 추상화하여 동적으로 자원을 제어할 수 있음
OpenFlow를 지원하여 SDN Switch로 사용 가능
  OVSDB 프로토콜 지원
OVS의 설정 값을 저장한 DB를 관리하기 위한 프로토콜
터널링 프로토콜 지원 (GRE, VXLAN, IPsec 등)
모니터링 기능 지원 (NetFlow, sFlow, IPFIX, SPAN, RSPAN 등)
분산 가상 스위치 기능 제공
  다른 물리 서버에 위치한 가상 서버(VM)를 서로 연결
최신 버전 : 2.5.0 (2016/2/27)

## Slide 3: OVS 구조 및 관리 툴
OVS 커널모듈
OVS 데몬
datapath 관리툴
vSwitch를 제어를 위한 경량화 된 툴
ovsdb-server를 이용한 vswitch 관리 툴
OpenFlow를 이용한 OVS 관리 툴
ovsdb-server에
대한 CLI 제공
ovsdb 관리를 위한 CLI 제공
ovsdb를 관리하기 위한
RPC 인터페이스를 제공

## Slide 4: OVS Features
Visibility into inter-VM communication via NetFlow, sFlow(R), IPFIX, SPAN, RSPAN, and GRE-tunneled mirrors
LACP (IEEE 802.1AX-2008)
Standard 802.1Q VLAN model with trunking
Multicast snooping
IETF Auto-Attach SPBM and rudimentary required LLDP support
BFD and 802.1ag link monitoring
STP (IEEE 802.1D-1998) and RSTP (IEEE 802.1D-2004)
Fine-grained QoS control
Support for HFSC qdisc
Per VM interface traffic policing
NIC bonding with source-MAC load balancing, active backup, and L4 hashing
OpenFlow protocol support (including many extensions for virtualization)
IPv6 support
Multiple tunneling protocols (GRE, VXLAN, STT, and Geneve, with IPsec support)
Remote configuration protocol with C and Python bindings
Kernel and user-space forwarding engine options
Multi-table forwarding pipeline with flow-caching engine
Forwarding layer abstraction to ease porting to new software and hardware platforms

## Slide 5: Linux Bridge
Simple forwarding
Matches destination MAC address and forwards
Packet never leaves kernel

## Slide 6
감사합니다